## Slide 1: Chapter 1 An Introduction to Networking
Dr. Ning zhang

## Slide 2: Objectives
Identify types of applications and protocols used on a network
Distinguish between the client-server and peer-to-peer models used to control access to a network
Describe various networking hardware devices and the most common physical topologies

## Slide 3: Objectives
Describe the seven layers of the OSI model
Explore best practices for safety when working with networks and computers
Describe the seven-step troubleshooting model for solving a networking problem

## Slide 4: How Networks Are Used
Network services - the resources a network makes available to its users
  Includes applications and the data provided by these applications
Types of applications found on most networks:
  Client-Server
  File and Print Services
  Communications Services

## Slide 5: Client-Server Applications
Client computer requests data or a service from a second computer, called the server
List of several popular client-server applications:
  Web service – HTTP, HTTP+SSL/TLS=HTTPS
    Ex. Apache(UNIX), IIS (Windows)
  Email services – SMTP, POP3/IMAP4
  FTP service – no encryption, SFTP
    CuteFTP by GlobalSCAPE
  Telnet service - remote, no encryption, replaced by ssh
  Remote Desktop – Windows Remote Desktop (RDP), technician connection
  Remote applications – an application installed and executed on a server and presented to a user working at a client computer, RDP
Notes: HTTP – Hypertext Transfer Protocol
SSL- Secure Sockets Layer
TLS – Transport Layer Security
HTTPS- HTTP Secure
SMTP- Simple Mail Transfer Protocol
POP3- Post Office Protocol, Version 3
IMAP4, Internet Message Access Protocol, version4
FTP – File Transfer Protocol
SFTP- Secure File Transfer Protocol
SSH- Secure Shell
RDP – Remote Desktop Protocol

## Slide 6: Client-Server Applications
Notes: Client-Server Applications

## Slide 7: Client-Server Applications
Notes: Client-Server Applications

## Slide 8: File and Print Services
File services - a server’s ability to share data files and disk storage space
File server - a computer that provides file services
Print services - ability to share printers across a network
  With one printer, less time is spent on maintenance and management
  With one printer, less money is spent on maintenance and buying

## Slide 9: Communication Services
Convergence - using the same network to deliver multiple types of communications services
Unified communication (UC) - refers to the centralized management of multiple network-based communications
Three types of communication services:
  Conversational voice - VoIP (Voice over IP) – point-to-point model, point-to-multipoint
  Streaming live audio and video – client-server model, multicast distribution, RTP
  Streaming stored audio and video – client-server model
Notes: RTP- Real Time Transport Protocol

## Slide 10: Communication Services
Voice and video transmissions are delay-sensitive
  You don’t want to hear or see breaks in transmission
Voice and video transmission are considered loss-tolerant
Network administrators must pay attention to the quality of service (QoS) a network provides for voice and video
Bandwidth - the amount of traffic, or data transmission activity, on the network

## Slide 11: Controlling Network Access
Topology - how parts of a whole work together
Physical topology - mostly applies to hardware and describes how computers, other devices, and cables fir together to form the physical network
Logical topology - has to do with software and describes how access to the network is controlled
  How users and programs initially gain access to the network
Network operating system - controls access to the entire network
  Required by client-server models
  Ex. Windows Server 2012 R2, Ubuntu Server, Red Hat

## Slide 12: Peer-to-Peer Model
Peer-to-peer (P2P) network model - the OS of each computer on the network is responsible for controlling access to its resources
  No centralized control
Computers, called nodes or hosts, form a logical group of computers and users
  May share resources
  May prevent access to resources
Each computer user has a Windows local account
  Works only on that one computer
Notes: If all computers in a peer-to-peer network are running a Windows operating system, each computer has a Windows local account that works only on that one computer, Resources can be shared in these ways:
Using Windows folder and file sharing, each computer maintains a list of users and their rights on that particular PC. Windows allows a user on the network to access local resources based on these assigned rights.
Using a homegroup, each computer shares files, folders, libraries and printers with other computers in the homegroup. A homegroup limits how sharing can be controlled for individual users because any user of any computer in the homegroup can access homegroup resources.

## Slide 13: Peer-to-Peer Model
Notes: Peer-to-Peer Model

## Slide 14: Peer-to-Peer Model
Advantages
  Simple configuration
  Less expensive
    Compared to other network models
Disadvantages
  Not scalable
  Not necessarily secure
  Not practical for large installations

## Slide 15: Client-Server Network Model
Resources are managed by the network operating system (NOS) via a centralized directory database
Windows domain - a logical group of computers that a Windows Server can control
Active Directory (AD) - the centralized directory database that contains user account information and security for the entire group of computers
Global account (a.k.a. global username or network ID) - a domain-level account assigned by the network administrator and is kept in AD

## Slide 16: Client-Server Network Model
A user can sign on to the network from any computer on the network and gain access to the resources that AD allows
  This process is managed by Active Directory Domain Services (AD DS)
Clients don’t share their resources directly with each other
  Access is controlled by entries in the centralized domain database

## Slide 17: Client-Server Network Model
Notes: Client-Server Network Model

## Slide 18: Client-Server Network Model
The NOS is responsible for:
  Manages client data, resources
  Ensures authorized user access
  Controls user file access
  Restricts user network access
  Dictates computer communication rules
  Supplies application to clients
Server examples
  Windows Server 2012 R2, Ubuntu Server, or Red Hat Linux

## Slide 19: Client-Server Network Model
Servers that have a NOS installed require:
  More memory, processing, storage capacity
  Equipped with special hardware
    Provides network management functions
Advantages relative to peer-to-peer networks
  User credential assigned from one place
  Multiple shared resource access centrally controlled
  Central problem monitoring, diagnostics, correction capabilities
  More scalable

## Slide 20: Networking Hardware and Physical Topologies
Notes: Networking Hardware and Physical Topologies

## Slide 21: LANs and Their Hardware
Local area network (LAN) - usually contained in a small space
  Such as an office or building
Switch - receives incoming data from one of its ports and redirects it to another port or multiple ports
  Will send the data to its intended destination
Star topology - all devices connect to one central device (usually a switch)
Network interface card (NIC) - a network port used to attach a device to a network

## Slide 22: LANs and Their Hardware
A LAN can have several switches
Backbone - a central conduit that connects the segments (pieces) of a network
  Might use higher transmission speeds and different cabling than network cables connected to computers
Three switches daisy-chained together in a single line is said to use a bus topology
  However, each switch is connected to computers via a star topology, making it a star-bus topology
  A topology that combines topologies is known as a hybrid topology

## Slide 23: LANs and Their Hardware
Notes: LANs and Their Hardware

## Slide 24: LANs and Their Hardware
Router - a device that manages traffic between two or more networks
  Can help find the best path for traffic to get from one network to another
Routers can be used in small home networks to connect the home LAN to the Internet
Industrial-grade routers can have several network ports, one for each network it connects to
Difference between router and switch:
  Router is like a gateway between networks

## Slide 25: LANs and Their Hardware
Notes: LANs and Their Hardware

## Slide 26: MANs and WANs
Metropolitan area network (MAN) - a group of connected LANs in the same geographical area
  Also known as a campus area network (CAN)
WAN (wide area network) - a group of LANs that spread over a wide geographical area
  Internet is the largest and most varied WAN
MANs and WANs often use different transmission methods and media than LANs
PAN (personal area network) - smallest network
  A network of personal devices

## Slide 27: MANs and WANs
Notes: MANs and WANs

## Slide 28: Network Topology
https://www.youtube.com/watch?v=4AhsmW29J8M (Shows different topologies)
https://www.youtube.com/watch?v=SUfC311fke4 (May not need to show this)

## Slide 29: The Seven-Layer OSI Model
OSI (Open Systems Interconnection) reference model - a seven-layer model developed to categorize the layers of communication
Developed by ISO in the 1980s
The layers are numbered in order, starting with Layer 1, the Physical layer at the bottom
  Physical, Data Link, Network, Transport, Session, Presentation, Application
All People Seem to Need Data Processing

## Slide 30: The Seven-Layer OSI Model
Notes: The Seven-Layer OSI Model

## Slide 31: Layer 7: Application Layer
Application layer - describes the interface between two applications, on separate computers
Application layer protocols are used by programs that fall into two categories:
  Provide services to a user, such as a browser and Web server
  Utility programs that provide services to the system, such as SNMP (Simple Network Management Protocol) that monitor and gather information about network traffic and can alert network administrators about adverse conditions that need attention.
Payload - data that is passed between applications or utility programs and the OS

## Slide 32: Layer 6: Presentation Layer
Presentation layer - responsible for reformatting, compressing, and/or encrypting data in a way that the receiving application can read
Example:
  An email message can be encrypted at the Presentation layer by the email client or by the OS

## Slide 33: Layer 5: Session Layer
Session layer - describes how data between applications is synched and recovered if messages don’t arrive intact at the receiving application
The Application, Presentation, and Session layers are intertwined
  Often difficult to distinguish between them
Most tasks are performed by the OS when an application makes an API call to the OS
  Application programming interface (API) call is the method an application uses when it makes a request of the OS

## Slide 34: Layer 4: Transport Layer
Transport layer - responsible for transporting Application layer payloads from one application to another
Two main Transport layer protocols are:
  TCP (Transmission Control Protocol) - makes a connection with the end host, checks whether data was received; called a connection-oriented protocol
  UDP (User Datagram Protocol) - does not guarantee delivery by first connecting and checking whether data is received; called a connectionless protocol

## Slide 35: Layer 4: Transport Layer
Protocols add their own control information in an area at the beginning of the payload (called a header)
Encapsulation - process of adding a header to the data inherited from the layer above
The Transport layer header addresses the receiving application by a number called a port number
If message is too large, TCP divides it into smaller messages called segments
  In UDP, the message is called a datagram

## Slide 36: Layer 3: Network Layer
Network layer - responsible for moving messages from one node to another until reaches destination
IP adds its own Network layer header to the segment or datagram
  The entire Network layer message is called a packet
IP address - assigned to each node on a network
  Network layer uses it to uniquely identify each host
IP relies on several routing protocols to find the best route for a packet to take to reach destination
  ICMP and ARP are examples
Notes: ICMP – Internet Control Message Protocol

## Slide 37: Layer 2: Data Link Layer
Layers 2 and 1 are responsible for interfacing with physical hardware on the local network
  Protocols at these layers are programmed into firmware of a computer’s NIC and other hardware
Type of networking hardware or technology used on a network determine the Link Layer protocol used
  Ethernet and Wi-Fi are examples
The Link layer puts control information in a Link layer header and at the end of the packet in a trailer
  Entire Link layer is called a frame

## Slide 38: Layer 2: Data Link Layer
MAC (Media Access Control) address - hardware address of the source and destination NICs
  Also called a physical address, hardware address, or Data Link layer address
  Embedded on every network adapter and are considered short-range addresses that can only find nodes on the local network

## Slide 39: Layer 1: Physical Layer
Physical layer - simplest layer and is responsible for sending bits via a wired or wireless transmission
Can be transmitted as:
  Wavelengths in the air
  Voltage on a copper wire
  Light (via fiber-optic cabling)

## Slide 40: Protocol Data Unit or PDU
Protocol data unit (PDU) - the technical name for a group of bits as it moves from one layer to the next and from one LAN to the next
  Technicians loosely call this group of bits a message or a transmission

## Slide 41: Summary of How the Layers Work Together

## Slide 42: Summary of How the Layers Work Together
Notes: Summary of How the Layers Work Together

## Slide 43: OSI Model
https://www.youtube.com/watch?v=VGGmBhARuiY
https://www.youtube.com/watch?v=-6Uoku-M6oY
https://www.youtube.com/watch?v=X4XiTU81UBU&t=165s
https://www.youtube.com/watch?v=Kb4hVvlCx40

## Slide 44: OSI Model
Complete the following games – Time 40 minutes
https://goo.gl/7BuvKZ
https://goo.gl/FVxs1b
https://goo.gl/qzXScc
https://goo.gl/Yi3iyZ
Complete the following quizzes – Time 30 minutes
https://goo.gl/xjGMGw
https://goo.gl/Zqdcnf
https://goo.gl/XNgATa

## Slide 45: Staying Safe When Working with Networks and Computers
Network and computer technicians need to know how to protect themselves
  As well as protect sensitive electronic components
This section takes a look at some best practices for safety

## Slide 46: Emergency Procedures
Know the best escape route or emergency exit
Fire Suppression Systems - have a fire suppression system in the data center that includes:
  Emergency alert system
  Portable fire extinguishers
  Emergency power-off switch
  Suppression agent
Fail Open or Fail Close - does the security system allow access during a failure (fail open) or deny access during the failure (fail close)

## Slide 47: Emergency Procedures
Material Safety Data Sheet (MSDS) - explains how to properly handle substances such as chemical solvents and how to dispose of them
  Includes information such as physical data, toxicity, health effects, first aid, storage, shipping, disposal, and spill procedures

## Slide 48: HVAC Systems
Heating, ventilation, and air conditioning (HVAC) system - controls the environment in a data center
  Including the temperature, humidity, airflow, and air filtering
HVAC system must provide acceptable temperature and humidity ranges for devices that might overheat or fail due to high humidity
HVAC systems and network cabling often occupy the space above the ceiling or below the floor in a data center
  Called the plenum

## Slide 49: Protecting Against Static Electricity
Computer components are grounded inside a computer case
Sensitive electronic components can be damaged by electrostatic discharge (ESD)
Static electricity can cause two types of damage:
  Catastrophic failure - destroyed beyond use
  Upset failure - shorten the life of a component

## Slide 50: Protecting Against Static Electricity
Before touching a component, ground yourself by:
  Wearing an ESD strap around your wrist that clips onto the chassis or computer case
  Touching the case before touching any component inside the case
  Storing a component inside an antistatic bag
In addition to protecting against ESD, always shut down and unplug a computer before working inside it

## Slide 51: Installation Safety
Lifting Heavy Objects - follow these guidelines:
  Decide which side of object to face so load is most balanced
  Stand close to the object with your feet apart
  Keep your back straight, bend knees and grip load
  Lift with your legs, arms, and shoulders (not your back or stomach)
  Keep the load close to your body and avoid twisting your body while you’re holding it
  To put the object down, keep your back as straight as possible and lower object by bending your knees

## Slide 52: Installation Safety
Rack Installations - switches, routers, servers, and patch panels can be installed in racks
  Follow device manufacturer’s guidelines for requirements for the rack and the direction for installation

## Slide 53: Installation Safety
General directions for safely installing rack-mountable devices:
  Engage brakes on rack wheels, if applicable
  Wear an ESD strap
  Place the device in the rack for good airflow
  Device must be well grounded
  Pay attention to tools as you work so they don’t accidentally fall into a rack of expensive equipment
  Install fan trays so that air flows in the same direction as the fans inside the device

## Slide 54: Installation Safety
Notes: Installation Safety

## Slide 55: Electrical and Tool Safety in Data Centers
Electrical and tool safety is generally regulated by OSHA (Occupational Safety and Health Administration)
OSHA guidelines when using power tools:
  Wear personal protective equipment (PPE)
  Keep all tools in good condition and properly store tools not in use
  Use the right tool for the job and operate the tool according to the manufacturer’s instructions
  Watch out for trip hazards, so you and others don’t stumble on a tool or cord

## Slide 56: Troubleshooting Network Problems
Troubleshooting steps used by most expert networking troubleshooters:
  Identify problem
    Gather information
    Identify symptoms
    Question users
    Determine if anything has changed
  Establish theory of probable cause
    Question the obvious

## Slide 57: Troubleshooting Network Problems
Troubleshooting steps (cont’d)
  Test theory to determine cause
    If theory confirmed, determine next steps
    If theory not confirmed, establish new theory or escalate
  Establish action plan
  Implement solution or escalate the problem
  Verify full functionality
    Implement preventative measures if applicable
  Document findings, actions, outcomes

## Slide 58: Summary
Networks provide a wide range of services, including client-server applications, file and print services, and communications services
File and print services enable multiple users to share data, storage areas, and printers
Traditional peer-to-peer networks are usually simple and inexpensive to set up
The client-server model for access control relies on a centrally administered server using a NOS that manages shared resources for multiple clients
  More complex and expensive to install

## Slide 59: Summary
A LAN is a network of computers and other devices that can directly address all other nodes
In a star topology, all computers and network devices connect to one central device
A backbone is a central conduit that connects parts of a network and might use the bus topology
A router manages traffic between two or more LANS
LANS can be interconnected to form WANS, which traverse longer distances in two or more geographical areas

## Slide 60: Summary
The seven layers of the OSI model are Application, Presentation, Session, Transport, Network, Data Link, and Physical
At Layers 7,6, and 5, data and its control information is known as the payload
A message at the Transport layer is called a segment in TCP and a datagram in UDP
An IP transmission is called a packet
A message at the Data Link layer is called a frame
Some switches operate at the Data Link layer and routers operate at the Network layer

## Slide 61: Summary
A fire suppression system can include an emergency alert system, portable fire extinguishers, an emergency power-off switch, and suppression agents
HVAC systems are responsible for controlling humidity and temperature in a data center
When working with sensitive components, protect against ESD by using an ESD strap
Troubleshooting problems and their solutions are documented in a call tracking system

## Slide 62: In-Class exercise
The client-server network at Scoops, a chain of ice-cream stores, currently depends on one server machine running Windows Server 2008 as its NOS. However, the system was installed five years ago, and the chain is growing. The company’s general manager has heard a lot of good things about Linux operating systems – in particular, a type of Linux called Fedora/Ubuntu/Debian/Arch. He asks you to find out how these two NOSs differ in their file sharing, remote access, and mail service capabilities. Also, he wonders how the two compare in their ease of use, reliability and support. He remarks that he doesn't’t want to spend a lot of tome looking after the server, and reminds you that he is not a technical expert. After some research, what can you tell him about the similarities and differences between these two NOSs? Do you advise the Scoops chain to change its server’s NOS to Linux ? Why or why not?