## Slide 1: Chapter 2 How Computers Find Each Other on Networks
Dr. Sayonnha Mandal
Notes: Network+ Guide to Networks 7th Edition
Chapter 1
An Introduction to Networking

## Slide 2: Objectives
Describe how computers and other devices are addressed on a network
Explain how host names and domain names work
Identify how ports and sockets work at the OSI Transport layer
Demonstrate how IP addresses are assigned and formatted at the OSI Network layer
Use command-line tools to troubleshoot problems with network addresses
Notes: Objectives
Describe how computers and other devices are addressed on a network
Explain how host names and domain names work
Identify how ports and sockets work at the OSI Transport layer
Demonstrate how IP addresses are assigned and formatted at the OSI Network layer
Use command-line tools to troubleshoot problems with network addresses

## Slide 3: An Overview of Addressing on Networks
Four addressing methods:
  Application layer FQDNs, computer names, and host names
  Transport layer port numbers
  Network layer IP address
    IPv4 addresses have 32 bits and are written as four decimal numbers called octets
    IPv6 addresses have 128 bits and are written as eight blocks of hexadecimal numbers
  Data Link layer MAC address
    Also called physical address
Notes: An Overview of Addressing on Networks
Four addressing methods:
  Application layer FQDNs, computer names, and host names
  Transport layer port numbers
  Network layer IP address
    IPv4 addresses have 32 bits and are written as four decimal numbers called octets
    IPv6 addresses have 128 bits and are written as eight blocks of hexadecimal numbers
  Data Link layer MAC address
    Also called physical address

## Slide 4: MAC Addresses
Traditional MAC addresses contain two parts
  First 24 bits are known as the OUI (Organizationally Unique Identifier) or block ID or company-ID
    Assigned by the IEEE
  Last 24 bits make up the extension identifier or device ID
    Manufacturer’s assign each NIC a unique device ID
Notes: MAC Addresses
Traditional MAC addresses contain two parts
  First 24 bits are known as the OUI (Organizationally Unique Identifier) or block ID or company-ID
    Assigned by the IEEE
  Last 24 bits make up the extension identifier or device ID
    Manufacturer’s assign each NIC a unique device ID

## Slide 5: MAC Addresses
Notes: MAC Addresses

## Slide 6: How Host Names and Domain Names Work
Character-based names are easier to remember than numeric IP addresses
Last part of an FQDN is called the top-level domain (TLD)
Domain names must be registered with an Internet naming authority that works on behalf of ICANN
  ICANN restricts what type of hosts can be associated with .arpa, .mil, .int, .edu, and .gov
Name resolution is the process of discovering the IP address of a host when you know the FQDN
Notes: How Host Names and Domain Names Work
Character-based names are easier to remember than numeric IP addresses
Last part of an FQDN is called the top-level domain (TLD)
Domain names must be registered with an Internet naming authority that works on behalf of ICANN
  ICANN restricts what type of hosts can be associated with .arpa, .mil, .int, .edu, and .gov
Name resolution is the process of discovering the IP address of a host when you know the FQDN

## Slide 7: How Host Names and Domain Names Work
Notes: How Host Names and Domain Names Work

## Slide 8: DNS (Domain Name System)
DNS is an Application layer client-server system of computers and databases made up of these elements:
  namespace - the entire collection of computer names and their associated IP addresses stored in databases on DNS name servers around the globe
  name servers - hold databases, which are organized in a hierarchical structure
  resolvers - a DNS client that requests information from DNS name servers
Notes: DNS (Domain Name System)
DNS is an Application layer client-server system of computers and databases made up of these elements:
  namespace - the entire collection of computer names and their associated IP addresses stored in databases on DNS name servers around the globe
  name servers - hold databases, which are organized in a hierarchical structure
  resolvers - a DNS client that requests information from DNS name servers

## Slide 9: How Name Servers Are Organized
DNS name servers are organized in a hierarchical structure
At the root level, 13 clusters of root server hold information used to locate top-level domain (TLD) servers
TLD servers hold information about authoritative servers
  The authority on computer names and their IP address for computer in their domains
Notes: How Name Servers Are Organized
DNS name servers are organized in a hierarchical structure
At the root level, 13 clusters of root server hold information used to locate top-level domain (TLD) servers
TLD servers hold information about authoritative servers
  The authority on computer names and their IP address for computer in their domains

## Slide 10: How Name Servers Are Organized
Notes: How Name Servers Are Organized

## Slide 11: How Name Servers Are Organized
Notes: How Name Servers Are Organized

## Slide 12: How Name Servers Are Organized
Ways the resolution process can get more complex:
  Caching-only server - when it receives a request for information that is not stored in its DNS cache, it will first query the company’s authoritative name server
  Name servers within a company might not have access to root servers
  A TLD name server might be aware of an intermediate name server rather than the authoritative name server
Notes: How Name Servers Are Organized
Ways the resolution process can get more complex:
  Caching-only server - when it receives a request for information that is not stored in its DNS cache, it will first query the company’s authoritative name server
  Name servers within a company might not have access to root servers
  A TLD name server might be aware of an intermediate name server rather than the authoritative name server

## Slide 13: Recursive and Iterative Queries
Two types of DNS requests:
  Recursive - a query that demands a resolution or the answer “It can’t be found”
  Iterative - a query where the local server issues queries to other servers
    Other servers only provide information if they have it
    Do not demand a resolution
Notes: Recursive and Iterative Queries
Two types of DNS requests:
  Recursive - a query that demands a resolution or the answer “It can’t be found”
  Iterative - a query where the local server issues queries to other servers
    Other servers only provide information if they have it
    Do not demand a resolution

## Slide 14: DNS Zones and Zone Transfers
DNS follows a distributed database model
  Data is distributed over thousands of server so that DNS will not fail if one or a handful of servers experience errors
DNS zone - the domains an organization is responsible for managing
Primary DNS server holds the authoritative DNS database for the organization
Zone transfer - the process where a secondary DNS server makes a request to the primary server for a database update
Notes: DNS Zones and Zone Transfers
DNS follows a distributed database model
  Data is distributed over thousands of server so that DNS will not fail if one or a handful of servers experience errors
DNS zone - the domains an organization is responsible for managing
Primary DNS server holds the authoritative DNS database for the organization
Zone transfer - the process where a secondary DNS server makes a request to the primary server for a database update

## Slide 15: DNS Server Software
BIND (Berkeley Internet Name Domain) - most popular DNS server software
  Open source - the term for software whose code is publicly available for use and modification
Microsoft DNS Server - built-in DNS service in the Windows Server OS
Split DNS design - Internal and external DNS queries are handled by different DNS servers
  Also called a split-horizon DNS
Notes: DNS Server Software
BIND (Berkeley Internet Name Domain) - most popular DNS server software
  Open source - the term for software whose code is publicly available for use and modification
Microsoft DNS Server - built-in DNS service in the Windows Server OS
Split DNS design - Internal and external DNS queries are handled by different DNS servers
  Also called a split-horizon DNS

## Slide 16: DNS Server Software
Notes: DNS Server Software

## Slide 17: How a Namespace Database is Organized
Several types of records, called resource records are kept in a DNS database:
  A (Address) record - stores the name-to-address mapping for a host
  AAAA (Address) record - holds the name-to-address mapping, the IP address is an IPv6 type IP address
  CNAME (Canonical Name) record - holds alternative names for a host
  PTR (Pointer) record - used for reverse lookups
  MX (Mail Exchanger) record - identifies a mail server and is used for email traffic
Notes: How a Namespace Database is Organized
Several types of records, called resource records are kept in a DNS database:
  A (Address) record - stores the name-to-address mapping for a host
  AAAA (Address) record - holds the name-to-address mapping, the IP address is an IPv6 type IP address
  CNAME (Canonical Name) record - holds alternative names for a host
  PTR (Pointer) record - used for reverse lookups
  MX (Mail Exchanger) record - identifies a mail server and is used for email traffic

## Slide 18: DDNS (Dynamic DNS)
DDNS - a protocol used along with monitoring software to monitor the IP addresses dynamically assigned to your home network by your ISP
  Manages dynamic updates to its DNS records for domain names for home Web sites
Home routers sometimes provide the monitoring software embedded in the router firmware
Notes: DDNS (Dynamic DNS)
DDNS - a protocol used along with monitoring software to monitor the IP addresses dynamically assigned to your home network by your ISP
  Manages dynamic updates to its DNS records for domain names for home Web sites
Home routers sometimes provide the monitoring software embedded in the router firmware

## Slide 19: How Ports and Sockets Work
Port numbers - ensure data is transmitted to the correct application
Socket - consists of host’s IP address and the port number of an application running on the host
  Colon separates the two values
  Example - 10.43.3.87:23
Port numbers are divided into three types:
  Well-known ports - 0 to 1023
  Registered ports - 1024 to 49151
  Dynamic and private ports - 49152 to 65535
Notes: 1109 – Kerberos authentication protocol
1293 – IPSec encryption protocol

## Slide 20: How Ports and Sockets Work
Notes: When the host receives a request to communicate on port 23, it establishes or opens a session for communication with the Telnet service and the socket is said to be open. When the TCP session is complete, the socket is closed or dissolved. You can think of. Socket as a virtual circuit between a server and client.

## Slide 21: How IP Addresses Are Formatted and Assigned
Two types of IP addresses:
  IPv4 - a 32-bit address
  IPv6 - a 128-bit address
Notes: How IP Addresses Are Formatted and Assigned
Two types of IP addresses:
  IPv4 - a 32-bit address
  IPv6 - a 128-bit address

## Slide 22: How IPv4 Addresses Are Formatted and Assigned
IPv4 addresses
  32-bit address organized into four groups of 8 bits each (known as octets)
  Each of the four octets can be any number from 0 to 255
  Some IP addresses are reserved
Notes: How IPv4 Addresses Are Formatted and Assigned
IPv4 addresses
  32-bit address organized into four groups of 8 bits each (known as octets)
  Each of the four octets can be any number from 0 to 255
  Some IP addresses are reserved

## Slide 23: Classes of IP Addresses
IPv4 addresses are divided into five classes:
  Class A, Class B, Class C, Class D, and Class E
When class licenses were available from IANA:
  Class A license was for a single octet
  Class B license was for the first two octets
  Class C license was for the first three octets
  Class D and Class E addresses were not available for general use
    Class D begin with 224-239 and are used for multicasting and Class E begin with octets 240-254 and are used for research
Notes: Classes of IP Addresses
IPv4 addresses are divided into five classes:
  Class A, Class B, Class C, Class D, and Class E
When class licenses were available from IANA:
  Class A license was for a single octet
  Class B license was for the first two octets
  Class C license was for the first three octets
  Class D and Class E addresses were not available for general use
    Class D begin with 224-239 and are used for multicasting and Class E begin with octets 240-254 and are used for research

## Slide 24: Classes of IP Addresses
Notes: Classes of IP Addresses

## Slide 25: Classes of IP Addresses
Notes: Classes of IP Addresses

## Slide 26: How a DHCP Server Assigns IP Addresses
Static IP addresses are assigned manually by the network administrator
Dynamic IP addresses are automatically assigned by a DHCP server
If a computer configured to use DHCP is unable to lease an IPv4 address from the DHCP server
  It uses an Automatic Private IP Addressing (APIPA) address in the address range 169.254.0.1 through 169.254.255.254
Notes: How a DHCP Server Assigns IP Addresses
Static IP addresses are assigned manually by the network administrator
Dynamic IP addresses are automatically assigned by a DHCP server
If a computer configured to use DHCP is unable to lease an IPv4 address from the DHCP server
  It uses an Automatic Private IP Addressing (APIPA) address in the address range 169.254.0.1 through 169.254.255.254

## Slide 27: Public and Private IP Addresses
Class A, B, and C licensed IP addresses are available for use on the Internet
  Called public IP addresses
A company can use private IP addresses on its private networks
IEEE recommends the following IP addresses be used for private networks:
  10.0.0.0 through 10.255.255.255
  172.16.0.0 through 172.31.255.255
  192.168.0.0 through 192.168.255.255
Notes: Public and Private IP Addresses
Class A, B, and C licensed IP addresses are available for use on the Internet
  Called public IP addresses
A company can use private IP addresses on its private networks
IEEE recommends the following IP addresses be used for private networks:
  10.0.0.0 through 10.255.255.255
  172.16.0.0 through 172.31.255.255
  192.168.0.0 through 192.168.255.255

## Slide 28: Address Translation, NAT, and PAT
Network Address Translation (NAT) - a technique designed to conserve public IP addresses needed by a network
Address translation - process where a gateway device substitutes the private IP addresses with its own public address
  When these computers need access to other networks or Internet
Port Address Translation (PAT) - process of assigning a TCP port number to each ongoing session between a local host and Internet host
Notes: Address Translation, NAT, and PAT
Network Address Translation (NAT) - a technique designed to conserve public IP addresses needed by a network
Address translation - process where a gateway device substitutes the private IP addresses with its own public address
  When these computers need access to other networks or Internet
Port Address Translation (PAT) - process of assigning a TCP port number to each ongoing session between a local host and Internet host

## Slide 29: Address Translation, NAT, and PAT
Notes: Address Translation, NAT, and PAT

## Slide 30: Address Translation, NAT, and PAT
Two variations of NAT to be aware of:
  SNAT (Static Network Address Translation) - the gateway assigns the same public IP address to a host each time it makes a request to access the Internet
  DNAT (Dynamic Network Address Translation) - the gateway has a pool of public address that it is free to assign to a local host when it makes a request to access the Internet
Notes: Address Translation, NAT, and PAT
Two variations of NAT to be aware of:
  SNAT (Static Network Address Translation) - the gateway assigns the same public IP address to a host each time it makes a request to access the Internet
  DNAT (Dynamic Network Address Translation) - the gateway has a pool of public address that it is free to assign to a local host when it makes a request to access the Internet

## Slide 31: How IPv6 Addresses Are Formatted and Assigned
An IPv6 address has 128 bits written as eight blocks of hexadecimal numbers separated by colons
  Ex: 2001:0000:0B80:0000:0000:00D3:9C5A:00CC
  Each block is 16 bits
  Leading zeros in a four-character hex block can be eliminated
  If blocks contain all zeroes, they can be written as double colons (::), only one set of double colons is used in an IP address
  Therefore, above example can be written:
    2001:0000:B80::D3:9C5A:CC
Notes: How IPv6 Addresses Are Formatted and Assigned
An IPv6 address has 128 bits written as eight blocks of hexadecimal numbers separated by colons
  Ex: 2001:0000:0B80:0000:0000:00D3:9C5A:00CC
  Each block is 16 bits
  Leading zeros in a four-character hex block can be eliminated
  If blocks contain all zeroes, they can be written as double colons (::), only one set of double colons is used in an IP address
  Therefore, above example can be written:
    2001:0000:B80::D3:9C5A:CC

## Slide 32: How IPv6 Addresses Are Formatted and Assigned
IPv6 terminology:
  Link (sometimes called local link) - any LAN bounded by routers
  An interface is a node’s attachment to a link
  Tunneling - a method used by IPv6 to transport IPv6 packets through or over an IPv4 network
  Interface ID - the last 64 bits or four blocks of an IPv6 address that identify the interface
  Neighbors - two or more nodes on the same link
Notes: How IPv6 Addresses Are Formatted and Assigned
IPv6 terminology:
  Link (sometimes called local link) - any LAN bounded by routers
  An interface is a node’s attachment to a link
  Tunneling - a method used by IPv6 to transport IPv6 packets through or over an IPv4 network
  Interface ID - the last 64 bits or four blocks of an IPv6 address that identify the interface
  Neighbors - two or more nodes on the same link

## Slide 33: Types of IP Addresses
Unicast address - specifies a single node on a network
  Global unicast address - can be routed on the Internet
  Link local unicast address - can be used for communicating with nodes in the same link
Multicast address - packets are delivered to all nodes on a network
Anycast address - can identify multiple destinations, with packets delivered to the closest destination
Notes: Types of IP Addresses
Unicast address - specifies a single node on a network
  Global unicast address - can be routed on the Internet
  Link local unicast address - can be used for communicating with nodes in the same link
Multicast address - packets are delivered to all nodes on a network
Anycast address - can identify multiple destinations, with packets delivered to the closest destination

## Slide 34: Types of IP Addresses
Notes: Types of IP Addresses

## Slide 35: Types of IP Addresses
Notes: Types of IP Addresses

## Slide 36: Types of IP Addresses
Notes: Types of IP Addresses

## Slide 37: IPv6 Autoconfiguration
IPv6 addressing is designed so that a computer can autoconfigure its own link local IP address
  Similar to how IPv4 uses an APIPA address
Step 1 - The computer creates its IPv6 address
  Uses FE80::/64 as the first 64 bits
  Last 64 bits can be generated in two ways:
    Randomly generated
    Generated from the network adapter’s MAC address
Step 2 - The computer checks to make sure its IP address is unique on the network
Notes: IPv6 Autoconfiguration
IPv6 addressing is designed so that a computer can autoconfigure its own link local IP address
  Similar to how IPv4 uses an APIPA address
Step 1 - The computer creates its IPv6 address
  Uses FE80::/64 as the first 64 bits
  Last 64 bits can be generated in two ways:
    Randomly generated
    Generated from the network adapter’s MAC address
Step 2 - The computer checks to make sure its IP address is unique on the network

## Slide 38: IPv6 Autoconfiguration
Step 3 - The computer asks if a router on the network can provide configuration information
  If a router responds with DHCP information, the computer uses whatever information this might be
    Such as the IP addresses of DNS server or the network prefix
If the network prefix is supplied, this will become the first 64 bits of its own IP address
  Process is called prefix discovery
Notes: IPv6 Autoconfiguration
Step 3 - The computer asks if a router on the network can provide configuration information
  If a router responds with DHCP information, the computer uses whatever information this might be
    Such as the IP addresses of DNS server or the network prefix
If the network prefix is supplied, this will become the first 64 bits of its own IP address
  Process is called prefix discovery

## Slide 39: Tunneling
Dual stacked - term given when a network is configured to use both IPv4 and IPv6 protocols
If packets on this network must traverse other networks where dual stacking is not used, tunneling is used
Three tunneling protocols:
  6to4
  ISATAP (Intra-Site Automatic Tunnel Addressing)
  Teredo
Notes: Tunneling
Dual stacked - term given when a network is configured to use both IPv4 and IPv6 protocols
If packets on this network must traverse other networks where dual stacking is not used, tunneling is used
Three tunneling protocols:
  6to4
  ISATAP (Intra-Site Automatic Tunnel Addressing)
  Teredo

## Slide 40: Tunneling Contd.
6to4:
  Most common
  Always begins with same 16bit prefix (called fixed bits), which is 2002
  Prefix written as 2002::/16
  Next 32 bits are the 32 bits of the IPv4 address of the sending host
ISATAP:
  works only on single organization’s intranet
  By default enabled in Windows 7 and 8.1
Teredo:
  named after teredo worm (bores holes in wood)
  Address always begins with 2001
  Prefix written as 2001::/32
  Enabled by default in Windows 7. not 8.1
  Unix and Linux supports Miredo (third party software)

## Slide 41: Tunneling
Notes: Routers A, C, D and Z are configured to use the 4to6 protocol to tunnel IPv4 packets that arrive from outside the intranet at gateway routers A or Z and are routed through the 4to6 tunnel to the other side of the intranet.

## Slide 42: Tools for Troubleshooting IP Address Problems
Event Viewer - one of the first places to start looking for clues when something goes wrong
Notes: Provides lot of valuable information about the problems the computer is experiencing and even make suggestions for what to do next.

## Slide 43: ping
ping (Packet Internet Groper) - used to verify that TCP/IP is installed, bound to the NIC, configured correctly, and communicating with the network
The ping utility sends out a signal called an echo request to another device (request for a response)
  Other computer responds in the form of an echo reply
ICMP - protocol used by the echo request/reply to carry error messages and information about the network
Notes: ping
ping (Packet Internet Groper) - used to verify that TCP/IP is installed, bound to the NIC, configured correctly, and communicating with the network
The ping utility sends out a signal called an echo request to another device (request for a response)
  Other computer responds in the form of an echo reply
ICMP - protocol used by the echo request/reply to carry error messages and information about the network

## Slide 44: ping

## Slide 45: ping
IPv6 networks use a version of ICMP called ICMPv6
  ping6 - on Linux computers running IPv6, use ping6 to verify whether an IPv6 host is available
  ping -6 - on Windows computers, use ping with the -6 switch to verify connectivity on IPv6 networks
For the ping6 and ping -6 commands to work over the Internet, you must have access to the IPv6 Internet
Notes: ping
IPv6 networks use a version of ICMP called ICMPv6
  ping6 - on Linux computers running IPv6, use ping6 to verify whether an IPv6 host is available
  ping -6 - on Windows computers, use ping with the -6 switch to verify connectivity on IPv6 networks
For the ping6 and ping -6 commands to work over the Internet, you must have access to the IPv6 Internet

## Slide 46: ipconfig
Notes: ipconfig

## Slide 47: ifconfig
ifconfig - utility to view and manage TCP/IP settings
If your Linux or UNIX system provides a GUI
  Open a shell prompt, then type ifconfig
Notes: ifconfig
ifconfig - utility to view and manage TCP/IP settings
If your Linux or UNIX system provides a GUI
  Open a shell prompt, then type ifconfig

## Slide 48: nslookup
nslookup (name space lookup) - allows you to query the DNS database from any computer on a network
  To find the host name of a device by specifying its IP address, or vice versa
  Useful for verifying a host is configured correctly or for troubleshooting DNS resolution problems
Reverse DNS lookup - to find the host name of a device whose IP address you know
Two modes:
  Interactive - to test multiple DNS servers at one time
  Noninteractive - test a single DNS server
Notes: nslookup
nslookup (name space lookup) - allows you to query the DNS database from any computer on a network
  To find the host name of a device by specifying its IP address, or vice versa
  Useful for verifying a host is configured correctly or for troubleshooting DNS resolution problems
Reverse DNS lookup - to find the host name of a device whose IP address you know
Two modes:
  Interactive - to test multiple DNS servers at one time
  Noninteractive - test a single DNS server

## Slide 49: nslookup
Notes: nslookup

## Slide 50: nslookup
You can change DNS servers from within interactive mode with the server subcommand and specifying the IP address of the new DNS server
To exit nslookup’s interactive mode, enter exit
Notes: nslookup
You can change DNS servers from within interactive mode with the server subcommand and specifying the IP address of the new DNS server
To exit nslookup’s interactive mode, enter exit

## Slide 51: Summary
Hosts on a network are assigned host names
Applications are assigned one or more port numbers to communicate with other applications
IPv4 addresses have 32 bits and are written as four decimal numbers called octets
IPv6 addresses have 128 bits and are written as eight blocks of hexadecimal numbers
Every NIC is assigned a unique 48-bit MAC address
Use the ipconfig command to view IP configuration information
Notes: Summary
Hosts on a network are assigned host names
Applications are assigned one or more port numbers to communicate with other applications
IPv4 addresses have 32 bits and are written as four decimal numbers called octets
IPv6 addresses have 128 bits and are written as eight blocks of hexadecimal numbers
Every NIC is assigned a unique 48-bit MAC address
Use the ipconfig command to view IP configuration information

## Slide 52: Summary
A FQDN includes both a host name portion and a domain name portion
Name resolution is the process of matching an FQDN to its IP address
DNS is an automated name resolution service that operates at the Application layer
DNS data is spread throughout the globe in a distributed database model
An IP address and a port number written together is called a socket
Notes: Summary
A FQDN includes both a host name portion and a domain name portion
Name resolution is the process of matching an FQDN to its IP address
DNS is an automated name resolution service that operates at the Application layer
DNS data is spread throughout the globe in a distributed database model
An IP address and a port number written together is called a socket

## Slide 53: Summary
Well-known ports range from 0 to 1023 and are assigned by IANA
You can define a range of available IP addresses in DHCP, or assign a static IP address as a DHCP reservation
NAT is used to allow devices that have private IP addresses access to the Internet
Tunneling protocols are used to allow IPv6 packets to travel over or through an IPv4 network
Three types of IPv6 addresses are unicast, multicast, and anycast addresses
Notes: Summary
Well-known ports range from 0 to 1023 and are assigned by IANA
You can define a range of available IP addresses in DHCP, or assign a static IP address as a DHCP reservation
NAT is used to allow devices that have private IP addresses access to the Internet
Tunneling protocols are used to allow IPv6 packets to travel over or through an IPv4 network
Three types of IPv6 addresses are unicast, multicast, and anycast addresses

## Slide 54: Summary
The ping utility uses ICMP to verify that TCP/IP is installed, bound to the NIC, configured correctly, and communicating with the network
ipconfig is useful for viewing and adjusting a Windows computer’s TCP/IP settings
On UNIX and Linux systems, the ifconfig utility is used to view and manage TCP/IP settings
The nslookup utility allows you to query the DNS database from any computer on the network
Notes: Summary
The ping utility uses ICMP to verify that TCP/IP is installed, bound to the NIC, configured correctly, and communicating with the network
ipconfig is useful for viewing and adjusting a Windows computer’s TCP/IP settings
On UNIX and Linux systems, the ifconfig utility is used to view and manage TCP/IP settings
The nslookup utility allows you to query the DNS database from any computer on the network