## Slide 1: Chapters 4 and 5

## Slide 2: NAS (Network Attached Storage)
Fault tolerance - techniques that allow data storage or other operations to continue in the event of a failure or fault of one its components
NAS - a specialized storage device or group of storage devices that provides centralized fault tolerant data storage for a network
  Contains its own file system optimized for saving and serving files
  Reads and writes from its disk significantly faster than other types of servers
  Can be easily expanded without interrupting service
Notes: NAS (Network Attached Storage)
Fault tolerance - techniques that allow data storage or other operations to continue in the event of a failure or fault of one its components
NAS - a specialized storage device or group of storage devices that provides centralized fault tolerant data storage for a network
  Contains its own file system optimized for saving and serving files
  Reads and writes from its disk significantly faster than other types of servers
  Can be easily expanded without interrupting service

## Slide 3: NAS (Network Attached Storage)
A NAS device cannot communicate directly with clients
  Clients go through a file server, which communicates with the NAS device
Notes: NAS (Network Attached Storage)
A NAS device cannot communicate directly with clients
  Clients go through a file server, which communicates with the NAS device

## Slide 4: SANs (Storage Area Networks)
A SAN is a network of storage devices that communicate directly with each other and with other networks
  Uses a type of architecture that is similar to mesh topology, which is very fault-tolerant
SANS use one of two types of Transport layer protocols:
  Fibre Channel (FC) – transport layer protocol used on fiber-optic media instead of TCP or UDP. Fiber channel connects devices within the SAN and also connects the SAN to other networks.
  iSCSI – (Internet SCSI) is a transport layer protocol that runs on top of TCP to allow fast transmissions over LANs, WANs and the Internet. It can work on a twisted pair Ethernet network with ordinary Ethernet NICs.
Notes: SANs (Storage Area Networks)
A SAN is a network of storage devices that communicate directly with each other and with other networks
  Uses a type of architecture that is similar to mesh topology, which is very fault-tolerant
SANS use one of two types of Transport layer protocols:
  Fibre Channel (FC)
  iSCSI

## Slide 5: SANs (Storage Area Networks)
Notes: SANs (Storage Area Networks)

## Slide 6: SANs (Storage Area Networks)
A SAN can be installed in a location separate from the LAN it serves
SANs are highly scalable and have:
  A very high fault tolerance
  Massive storage capabilities
  Fast data access
SANs are best suited to environments with huge quantities of data that must always be quickly available
Notes: SANs (Storage Area Networks)
A SAN can be installed in a location separate from the LAN it serves
SANs are highly scalable and have:
  A very high fault tolerance
  Massive storage capabilities
  Fast data access
SANs are best suited to environments with huge quantities of data that must always be quickly available

## Slide 7: NICs and Ethernet
Each workstation, server, printer, connectivity device, or other device on a network uses a NIC
On local networks, a NIC uses Ethernet standards for communication
Notes: NICs and Ethernet
Each workstation, server, printer, connectivity device, or other device on a network uses a NIC
On local networks, a NIC uses Ethernet standards for communication

## Slide 8: Characteristics of NICs
The NIC contains a transceiver that transmits and receives data signals over network media
NICs belong to both the Physical and Data Link layer because they:
  Issue data signals and assemble/disassemble data frames
  Interpret physical addressing information
  Perform routines that determine which node has the right to transmit data
  Can also perform prioritization, network management, buffering, and traffic-filtering functions
Notes: Characteristics of NICs
The NIC contains a transceiver that transmits and receives data signals over network media
NICs belong to both the Physical and Data Link layer because they:
  Issue data signals and assemble/disassemble data frames
  Interpret physical addressing information
  Perform routines that determine which node has the right to transmit data
  Can also perform prioritization, network management, buffering, and traffic-filtering functions

## Slide 9: Characteristics of NICs
NICs come in a variety of types depending on:
  Connection type
  Maximum network transmission speed
  Connector interfaces
  Number of connector interfaces, or ports
  Manufacturer
  Support for enhanced features, such as PoE+, buffering, or traffic management
  Method of interfacing with the computer’s motherboard and interface standards
Notes: Characteristics of NICs
NICs come in a variety of types depending on:
  Connection type
  Maximum network transmission speed
  Connector interfaces
  Number of connector interfaces, or ports
  Manufacturer
  Support for enhanced features, such as PoE+, buffering, or traffic management
  Method of interfacing with the computer’s motherboard and interface standards

## Slide 10: Characteristics of NICs
A NIC interfaces with a computer’s motherboard by one of the following methods:
  Integrated into the motherboard
  Installed in an expansion slot on the motherboard
  Installed as a peripheral device
Notes: Characteristics of NICs
A NIC interfaces with a computer’s motherboard by one of the following methods:
  Integrated into the motherboard
  Installed in an expansion slot on the motherboard
  Installed as a peripheral device

## Slide 11: Characteristics of NICs
Notes: Characteristics of NICs

## Slide 12: Characteristics of NICs
General tips when installing NICs:
  Install hardware and software
  Install a peripheral NIC
  Install an expansion card NIC
  Install multiple NICs in servers and other high-powered computers
Notes: Characteristics of NICs
General tips when installing NICs:
  Install hardware and software
  Install a peripheral NIC
  Install an expansion card NIC
  Install multiple NICs in servers and other high-powered computers

## Slide 13: Simplex, Half-Duplex, and Duplex
Methods of transmission:
  Full-duplex, also called duplex - signals are free to travel in both directions over a medium simultaneously
  Half-duplex - signals may travel in both directions over a medium but in only one direction at a time
  Simplex - signals may travel in only one direction
    Sometimes called one-way or unidirectional
Many network devices allow you to specify whether the device should use half- or full-duplex
  Modern NICs use full-duplex by default
Notes: Simplex, Half-Duplex, and Duplex
Methods of transmission:
  Full-duplex, also called duplex - signals are free to travel in both directions over a medium simultaneously
  Half-duplex - signals may travel in both directions over a medium but in only one direction at a time
  Simplex - signals may travel in only one direction
    Sometimes called one-way or unidirectional
Many network devices allow you to specify whether the device should use half- or full-duplex
  Modern NICs use full-duplex by default

## Slide 14: Simplex, Half-Duplex, and Duplex
Auto Negotiation - allows the NIC to select the best link speed and duplex that is also supported by the neighboring device
If you specify a particular speed and duplex that is not supported by a neighboring device
  The result is a speed and duplex mismatch and transmission will fail
Using UNIX or Linux, the ethtool utility allows you to view and change NIC settings
Notes: Simplex, Half-Duplex, and Duplex
Auto Negotiation - allows the NIC to select the best link speed and duplex that is also supported by the neighboring device
If you specify a particular speed and duplex that is not supported by a neighboring device
  The result is a speed and duplex mismatch and transmission will fail
Using UNIX or Linux, the ethtool utility allows you to view and change NIC settings

## Slide 15: Co-axial cable
Co-axial cable has a central metal core (often copper) surrounded by an insulator, a braided metal shielding called braiding or shield and an outer cover called the sheath or jacket.
The core can have a solid metal wire or several thin strands of metal wire and carries the electromagnetic signal.
The shielding protects the signal against noise and is a ground for the signal.
The plastic insulator can be PVC (polyvinyl chloride) or Teflon and protects the code from the metal shielding because if the two made contact, the wire would short-circuit.

## Slide 16: Twisted-Pair Cable
Color-coded insulated copper wire pairs
  0.4 to 0.8 mm diameter
  Encased in a plastic sheath
  Every two wires are twisted
  together
Notes: Twisted-Pair Cable
Color-coded insulated copper wire pairs
  0.4 to 0.8 mm diameter
  Encased in a plastic sheath
  Every two wires are twisted
  together

## Slide 17: Twisted-Pair Cable
More wire pair twists per foot
  More resistance to cross talk
  Higher-quality
  More expensive
Twist ratio
  Twists per meter or foot
High twist ratio
  Greater attenuation
Notes: Twisted-Pair Cable
More wire pair twists per foot
  More resistance to cross talk
  Higher-quality
  More expensive
Twist ratio
  Twists per meter or foot
High twist ratio
  Greater attenuation

## Slide 18: Twisted-Pair Cable
Hundreds of different designs
  Twist ratio, number of wire pairs, copper grade, shielding type, shielding materials
  1 to 4200 wire pairs possible
Wiring standard specification
  TIA/EIA 568
Most common twisted pair types
  Category (cat) 3, 5, 5e, 6, 6a, 7
  CAT 5e or higher used in modern LANs
Notes: Twisted-Pair Cable
Hundreds of different designs
  Twist ratio, number of wire pairs, copper grade, shielding type, shielding materials
  1 to 4200 wire pairs possible
Wiring standard specification
  TIA/EIA 568
Most common twisted pair types
  Category (cat) 3, 5, 5e, 6, 6a, 7
  CAT 5e or higher used in modern LANs

## Slide 19: Twisted-Pair Cable
Advantages
  Relatively inexpensive
  Flexible
  Easy installation
  Spans significant distance before requiring repeater
  Accommodates several different topologies
Two categories
  Shielded twisted pair (STP)
  Unshielded twisted pair (UTP)
Notes: Twisted-Pair Cable
Advantages
  Relatively inexpensive
  Flexible
  Easy installation
  Spans significant distance before requiring repeater
  Accommodates several different topologies
Two categories
  Shielded twisted pair (STP)
  Unshielded twisted pair (UTP)

## Slide 20: STP (Shielded Twisted Pair)
Individually insulated
Surrounded by metallic substance shielding (foil)
  Barrier to external electromagnetic forces
  Contains electrical energy of signals inside
  May be grounded
Notes: STP (Shielded Twisted Pair)
Individually insulated
Surrounded by metallic substance shielding (foil)
  Barrier to external electromagnetic forces
  Contains electrical energy of signals inside
  May be grounded

## Slide 21: UTP (Unshielded Twisted Pair)
One or more insulated wire pairs
  Encased in plastic sheath
  No additional shielding
    Less expensive, less noise resistance
Notes: UTP (Unshielded Twisted Pair)
One or more insulated wire pairs
  Encased in plastic sheath
  No additional shielding
    Less expensive, less noise resistance

## Slide 22: Comparing STP and UTP
Throughput
  STP and UTP can transmit the same rates
Cost
  STP and UTP vary in cost
Connector
  STP and UTP use Registered Jack 45
Noise immunity
  STP more noise resistant
Size and scalability
  Maximum segment length for both: 100 meters
Notes: Comparing STP and UTP
Throughput
  STP and UTP can transmit the same rates
Cost
  STP and UTP vary in cost
Connector
  STP and UTP use Registered Jack 45
Noise immunity
  STP more noise resistant
Size and scalability
  Maximum segment length for both: 100 meters

## Slide 23: Ethernet Standards for Twisted-Pair Cabling
Notes: Ethernet Standards for Twisted-Pair Cabling

## Slide 24: Cable Pinouts
Proper cable termination is a requirement for two nodes on a network to communicate
TIA/EIA specifies two methods of inserting wires into RJ-45 plugs
  TIA/EIA 568A
  TIA/EIA 568B
No functional difference between the two standards
  Just make sure you use the same standard on every RJ-45 plug and jack
Notes: Cable Pinouts
Proper cable termination is a requirement for two nodes on a network to communicate
TIA/EIA specifies two methods of inserting wires into RJ-45 plugs
  TIA/EIA 568A
  TIA/EIA 568B
No functional difference between the two standards
  Just make sure you use the same standard on every RJ-45 plug and jack

## Slide 25: Cable Pinouts
Notes: Cable Pinouts

## Slide 26: Cable Pinouts
Straight-through cable
  Terminate RJ-45 plugs at both ends identically
Crossover cable
  Transmit and receive wires on one end reversed
Rollover cable
  All wires are reversed
  Terminations are a mirror image of each other
  Also called Yost cables or Cisco console cables
  Used to connect a computer to the console port of a router
Notes: Cable Pinouts
Straight-through cable
  Terminate RJ-45 plugs at both ends identically
Crossover cable
  Transmit and receive wires on one end reversed
Rollover cable
  All wires are reversed
  Terminations are a mirror image of each other
  Also called Yost cables or Cisco console cables
  Used to connect a computer to the console port of a router

## Slide 27: Fiber-Optic Cable
Fiber-optic cable (fiber)
  One or more glass or plastic fibers at its center (core)
Data transmission
  Pulsing light sent from laser or light-emitting diode (LED) through central fibers
Cladding
  Layer of glass or plastic surrounding fibers
  Different density from glass or plastic in strands
  Reflects light back to core
  Allows fiber to bend
Notes: Fiber-Optic Cable
Fiber-optic cable (fiber)
  One or more glass or plastic fibers at its center (core)
Data transmission
  Pulsing light sent from laser or light-emitting diode (LED) through central fibers
Cladding
  Layer of glass or plastic surrounding fibers
  Different density from glass or plastic in strands
  Reflects light back to core
  Allows fiber to bend

## Slide 28: Fiber-Optic Cable
Plastic buffer outside cladding
  Protects cladding and core
  Opaque to absorb escaping light
  Surrounded by Kevlar (polymeric fiber) strands
Plastic sheath covers Kevlar strands
Notes: Fiber-Optic Cable
Plastic buffer outside cladding
  Protects cladding and core
  Opaque to absorb escaping light
  Surrounded by Kevlar (polymeric fiber) strands
Plastic sheath covers Kevlar strands

## Slide 29: Fiber-Optic Cable
Benefits over copper cabling
  Extremely high throughput
  Very high noise resistance
  Excellent security
  Able to carry signals for longer distances
  Industry standard for high-speed networking
Drawbacks
  More expensive than twisted pair cable
  Requires special equipment to splice
Notes: Fiber-Optic Cable
Benefits over copper cabling
  Extremely high throughput
  Very high noise resistance
  Excellent security
  Able to carry signals for longer distances
  Industry standard for high-speed networking
Drawbacks
  More expensive than twisted pair cable
  Requires special equipment to splice

## Slide 30: Fiber-Optic Cable
Throughput
  Proven reliable in transmitting data at rates that can reach 100 gigabits per second per channel
Cost
  Most expensive transmission medium
Noise immunity
  Unaffected by EMI
Size and scalability
  Segment lengths vary from 150 to 40,000 meters
  Depends on the light’s wavelength and type of cable
Notes: Fiber-Optic Cable
Throughput
  Proven reliable in transmitting data at rates that can reach 100 gigabits per second per channel
Cost
  Most expensive transmission medium
Noise immunity
  Unaffected by EMI
Size and scalability
  Segment lengths vary from 150 to 40,000 meters
  Depends on the light’s wavelength and type of cable

## Slide 31: SMF (Single Mode Fiber)
Consists of narrow core (8-10 microns in diameter)
  Laser-generated light travels over one path
    Little reflection
  Light does not disperse as signal travels
Can carry signals many miles:
  Before repeating is required
Rarely used for shorter connections
  Due to cost
  The Internet backbone depends on SMF
Notes: SMF (Single Mode Fiber)
Consists of narrow core (8-10 microns in diameter)
  Laser-generated light travels over one path
    Little reflection
  Light does not disperse as signal travels
Can carry signals many miles:
  Before repeating is required
Rarely used for shorter connections
  Due to cost
  The Internet backbone depends on SMF

## Slide 32: MMF (Multimode Fiber)
Contains a core with a larger diameter than single mode fiber
  Common sizes: 50 or 62.5 microns
Laser or LED generated light pulses travel at different angles
Greater attenuation than single-mode fiber
Common uses
  Cables connecting router to a switch
  Cables connecting server on network backbone
Notes: MMF (Multimode Fiber)
Contains a core with a larger diameter than single mode fiber
  Common sizes: 50 or 62.5 microns
Laser or LED generated light pulses travel at different angles
Greater attenuation than single-mode fiber
Common uses
  Cables connecting router to a switch
  Cables connecting server on network backbone

## Slide 33: Transmission Flaws
Noise
  Any undesirable influence degrading or distorting signal
Types of noise
  EMI (electromagnetic interference)
    Example: radio frequency interference
  Cross-talk
    Signal on one wire infringes on adjacent wire signal
    Alien cross-talk occurs between two cables
    Near end cross-talk (NEXT) occurs near source
    Far end cross-talk (FEXT) occurs at the far end
Notes: Transmission Flaws
Noise
  Any undesirable influence degrading or distorting signal
Types of noise
  EMI (electromagnetic interference)
    Example: radio frequency interference
  Cross-talk
    Signal on one wire infringes on adjacent wire signal
    Alien cross-talk occurs between two cables
    Near end cross-talk (NEXT) occurs near source
    Far end cross-talk (FEXT) occurs at the far end

## Slide 34: Transmission Flaws
Notes: Transmission Flaws

## Slide 35: Transmission Flaws
Attenuation
  Loss of signal’s strength as it travels away from source
Two ways analog and digital signals are boosted:
  Amplifier - increases the voltage, or strength, of signals
    Can also boot the noise that has accumulated in the signal
  Repeater - regenerates a digital signal in its original form
    Without noise previously accumulated
Notes: Transmission Flaws
Attenuation
  Loss of signal’s strength as it travels away from source
Two ways analog and digital signals are boosted:
  Amplifier - increases the voltage, or strength, of signals
    Can also boot the noise that has accumulated in the signal
  Repeater - regenerates a digital signal in its original form
    Without noise previously accumulated

## Slide 36: Transmission Flaws
Notes: Transmission Flaws

## Slide 37: Transmission Flaws
Latency
  Delay between signal transmission and receipt
  May cause network transmission errors
Latency causes
  Cable length
  Intervening connectivity device
Round trip time (RTT)
  Time for packet to go from sender to receiver, then back from receiver to sender
Notes: Transmission Flaws
Latency
  Delay between signal transmission and receipt
  May cause network transmission errors
Latency causes
  Cable length
  Intervening connectivity device
Round trip time (RTT)
  Time for packet to go from sender to receiver, then back from receiver to sender

## Slide 38: Transmission Flaws
Common Fiber Cable Problems:
  Fiber type mismatch
    More of a fiber core mismatch
    Even same-mode cables can be mismatched if the cores have different widths
  Wavelength mismatch
    SMF, MMF, and POF (Plastic Optical Fiber) use different wavelengths
  Dirty connectors
    Signal loss and other errors can start to cause problems
Notes: Transmission Flaws
Common Fiber Cable Problems:
  Fiber type mismatch
    More of a fiber core mismatch
    Even same-mode cables can be mismatched if the cores have different widths
  Wavelength mismatch
    SMF, MMF, and POF (Plastic Optical Fiber) use different wavelengths
  Dirty connectors
    Signal loss and other errors can start to cause problems